yaca
yet another CAN automation

technical manual

# Protocol definition
## General thoughts
The message-based structure of the CAN bus is used – messages are not adressed to a node, but have a number (the CAN message ID, in the following: „CANid“) identifying their usage. yaca uses extended CANids. These are assigned dynamically by the master node. The master node is used for setup, configuration and monitoring/logging, but the system must continue working even if the master fails.
In code, messages are simply implemented as C functions with a special prefix. A pre-/postprocessor then creates header files for including in code of other nodes, a function pointer table and CANid table in EEPROM for calling the functions when a message with a matching CANid is received. On the other hand, it also creates glue code in assembler to send a message when a remote message is „called“. This implements a simple RMI (remote method invocation) system which is supposed to make the code simple and logical.
avr-gcc is little-endian, but the message parameters are reversed while packing (avr-gcc rounds param adresses to 2, but the 8 bytes param of CAN messages are just too expensive for that) before transmission, the transmitted params are big-endian. On wire, any other numbers wider than 1 byte are represented as little-endian.
Despite being message-based, yaca still uses node identifiers (6-byte Boot-IDs) in configuration messages. The Boot-ID is hardcoded into the bootloader, effectively becoming a hardware address unique for each node.
## Master communication
Configuration mode is entered using messages with a special CANid, the Master-ID. The target is identified by the Boot-ID. Configuration mode simply refers to the Temp-ID being set and enabled, see below. After entering configuration mode, the node can be referred to with the Temp-ID, making it possible to transfer more bytes per CAN message.
A possibility exists to change the Master-ID (e.g. for using yaca on a CAN bus that has foreign nodes operating too), but it should not be done if not neccessary (if the Master-ID is lost, one can't enter the bootloader anymore). See Changing the Master-ID for details.
### Temp-ID association
This message is used to enter configuration mode – this is done by sending a temporary CANid (Temp-ID) to the target node which is then used for configuration messages later on. It sets a single byte of the Temp-ID at a time. If byten is 3 (4th byte), it also enables the Temp-ID. The frame is only valid if byten is between 0 and 3. The Temp-ID may only be stored in volatile memory (it must not be held after a power cycle).
CANid	0	1	2	3	4	5	6	7
Master-ID	byten	data	Boot-ID
	[0;3]

Message 1: Temp-ID association
If the master node is done with the configuration, it revokes the temporary CANid.
CANid	0	1	2	3	4	5	6	7
Temp-ID	0x01	d.c.

Message 2: Temp-ID revocation
The node then answers with:
CANid	0	1	2	3	4	5	6	7
Temp-ID	0x02	d.c.

Message 3: Temp-ID freed up
The master may then free up the temporary CANid internally. If the node doesn't reply, the master shouldn't free up the Temp-ID. Cleaning up is performed on Bus power-off.
### Network-ID
Each node transmits a Network-ID request on bootup, except when it receives such a request from another node (in which case it must cancel the transmission to stop flooding the bus).
CANid	0	1	2	3	4	5	6	7
Master-ID	0xFF	0x00	d.c.

Message 4: Network-ID request
On receipt of a Network-ID request, the master node broadcasts it, except when it wants to Hard-enter a bootloader.
CANid	0	1	2	3	4	5	6	7
Master-ID	0xFF	0x01	Network-ID

Message 5: Network-ID broadcast
### New nodes
If a node receives a Network-ID different from the ID stored in EEPROM, it has changed bus (it is now connected to a new bus). The node doesn't react on any stored CANids but informs the master node:
CANid	0	1	2	3	4	5	6	7
Master-ID	0xFF	0x02	Boot-ID

Message 6: New node
The node also tells the master node its device type:
CANid	0	1	2	3	4	5	6	7
Master-ID	0xFF	0x03	device type

Message 7: New node device type

When the user wishes to use the node on the new bus, the master node clears the old CANids and overwrites the Network-ID in the new node:
CANid	0	1	2	3	4	5	6	7
Master-ID	0xFF	0x04	Boot-ID

Message 8: Format node
### Bus power-off message
Some nodes may hold status information in volatile RAM (e.g. to conserve EEPROM write cycles). When powering off the bus on purpose, this message advises all nodes to save volatile information in non-volatile memory. After powering off the bus, the master may clear all Temp-IDs in memory.
CANid	0	1	2	3	4	5	6	7
Master-ID	0xFF	0xFF	d.c.

Message 9: Bus power-off broadcast
### Error messages
If the bootloader detects a wrong CRC after startup, it transmits a CRC error message:
CANid	0	1	2	3	4	5	6	7
Master-ID	0xFE	0x01	Boot-ID

Message 10: application CRC error
When the EEPROM overflows while writing the CANid data block, the node being programmed transmits a CANid data block address overflow:
CANid	0	1	2	3	4	5	6	7
Master-ID	0xFE	0x02	Boot-ID

Message 11: CANid data block address overflow
### Reading/writing the CANid data block
CANid data block write message:
CANid	0	1	2	3	4	5	6	7
Temp-ID	0x02	offset	count	data

Message 12: CANid data block write
CANids are stored in the CANid data block. The flash memory contains the neccessary function pointers. When a message is received, a loop goes through the list bytewise and matches the received CANid. An entry may contain several CANids, i.e. an additional Group-ID. The number of CANids for an entry is saved as the first byte.
CANid data block example (2 message functions): 02 01 23 45 67 12 34 56 78 01 23 45 67 89
The first message function is called when either CANid 01 23 45 67 or 12 34 56 78 is received.

It is important that the master node waits for a CANid data block write done message after writing the CANid data block with one or more data block write messages.
Single CANid read command – mi is the message index, ci the CANid sub-index (when ci is 0xFF, the command reads the count of CANids associated with a message):
CANid	0	1	2	3	4	5	6	7
Temp-ID	0x03	mi	ci	d.c.

Message 13: Single CANid read
The node sends a CANid reply:
CANid	0	1	2	3	4	5		6	7
Temp-ID	0x04	CANid/count (byte 1 only)					d.c.

Message 14: CANid reply
It is also possible to make a CANid data block read:
CANid	0	1	2	3	4	5	6	7
Temp-ID	0x05	offset	d.c.

Message 15: CANid data block read
The node sends a CANid data block reply (usually returns 7 bytes, except if the read offset was larger than EEPROM-size - CANid data block size - 7):
CANid	0	1	2	3	4	5	6	7
Temp-ID	0x06	data

Message 16: CANid data block reply
The CANid data block is cached in RAM to be able to execute fast consecutive writes. While the cache content differs from the data stored in EEPROM, a dirty flag is set in EEPROM. When the cache is completely flushed to EEPROM, the node clears the dirty flag and transmits a CANid data block write done message.
CANid	0	1	2	3	4	5	6	7
Temp-ID	0x07	d.c.

Message 17: CANid data block write done
### Changing the Master-ID
WARNING: If you lose the new Master-ID, you can't enter the bootloader anymore.
Out of security considerations, this message only works after Hard-entering the bootloader.
CANid	0	1	2	3	4	5		6	7
Temp-ID	0x08	new Master-ID					d.c.

Message 18: Change Master-ID
## Bootloader
The bootloader is used to update the firmware of a node without having to open the wall, box etc. where the node is located. It is the first program started on the microcontroller, for being able to download a new firmware even when the current firmware is bad. For this purpose, the bootloader waits a few seconds for a Temp-ID association after startup (bootloader time-out). After having received that, the bootloader will not start the application except when instructed to do so (by a Temp-ID revocation).
Before starting the firmware, the bootloader also checks its CRC-checksum to ensure firmware integrity (e.g. to detect if the firmware loading was interrupted).
### Entering the bootloader
This shall work in both application and bootloader when in configuration mode ( Temp-ID association sent). When executing the application, it jumps over to the bootloader section and tells the bootloader the current Temp-ID.
CANid	0	1	2	3	4	5	6	7
Temp-ID	0x09	d.c.

Message 19: Enter bootloader
### Hard-entering the bootloader
If the current application firmware is bad (wrong CRC or application error which prevents entering the bootloader), the master needs to hard-enter the bootloader. This is done by powering off the bus (see Bus power-off), waiting a few seconds until the buffer caps are discharged, re-applying power to the bus, waiting for the nodes to safely power up (e.g. 1 second less than bootloader time-out) and sending a Temp-ID association to enter configuration mode. As the bootloader section runs first on powerup, the bootloader can be entered even if the application is bad.
### Entering bootloader update
WARNING: If the newly programmed bootloader is not able to download a new bootloader, you have effectively locked yourself out. Check this before updating the bootloader.
WARNING: If power fails during a bootloader update (or if the bootstrap loader is running, even when not flashing), you have bricked the bootloader.
WARNING: The bootstrap loader is like a one-way street: you instantly have to download a new bootloader after having flashed it. There is no other way out that preserves the bootloader ability.
Do not use bootloader update. Never. You have been warned.
Out of security considerations, this message only works after Hard-entering the bootloader.
CANid	0	1	2	3	4	5	6	7
Temp-ID	0x0A	d.c.

Message 20: Enter bootloader update
Bootloader update is bound to a 512 Byte bootstrap program downloaded and started first, which then in turn downloads the actual bootloader. As this program must be very simple, the current version doesn't contain CAN controller initialization. Nothing useful will start after losing power. The bootstrap loader is downloaded as 8 pages. It may be located anywhere in the bootloader section (the current one has to be programmed at (relative) page 0) but must not overwrite the last 2 pages (the actual bootloader program which should never be updated). The bootloader may or may not send a Bootloader page done message after downloading the bootstrap loader.
### Programming
The application firmware memory is divided into pages. For the size of the pages or of the application flash, refer to the NDS. The memory is updated page-wise; first, select a page, then send data until the page is full. The page will automatically be programmed once all bytes are received. While programming a page, further data is ignored. After programming, the page counter will be incremented automatically; selecting further pages is only needed when leaving out pages while programming partially. When page programming is done, the node sends a Bootloader page done message.
The following message selects a page in the flash of the microcontroller:
CANid	0	1	2	3	4	5	6	7
Temp-ID	0x0B	page [le]		d.c.

Message 21: Bootloader page select
When downloading a bootloader, page counts as an offset from the start of the bootloader section. After a page is selected (or the page counter was incremented automatically), the master node sends the page data (the data pointer is advanced by the CAN message size):
CANid	0	1	2	3	4	5	6	7
Temp-ID	0x0C	data

Message 22: Bootloader page data
When the node has finished programming the page, it sends the following message:
CANid	0	1	2	3	4	5	6	7
Temp-ID	0x0D	d.c.

Message 23: Bootloader page done
After programming, a Temp-ID revocation tells the bootloader to calculate the application CRC.
For now, the Temp-ID is stored (fix) in EEPROM – to boot the app, the bootloader sends:
CANid	0	1	2	3	4	5	6	7
Temp-ID	0x0E	d.c.

Message 24: Boot application

# Node datasheet
The node datasheet (NDS) is an XML file containing information about a specific node firmware, e.g. message functions, EEPROM size, page size etc. These are needed by the master node.